## Slide 1: Power Load Forecasting
Park Jee Hyun
08 MAY 2017
-
SungKyunGwan University
Nanyang Technological University

## Slide 2: Contents
Purpose
Hypothesis
Experiments
Results
Think Backward
Conclusion

## Slide 3: Purpose
Accurate load forecasting is pivotal for the economic and secure operation of the power system
Goal: Achieving high load forecasting accuracy
Two main way to do this:
  improvement of the performance of the learning algorithm
  how well the data features are extracted through the pre-processing process.

## Slide 4: Hypothesis
H-ELM can outperform other Algorithms
  Various algorithms are being developed as research on artificial intelligence proceeds.
    Machine Learning(ML)
    Deep Learning(DL)
    Extreme Learning Machine(ELM)
    Hierarchical ELM(H-ELM)
  ML vs. ELM :
    Better efficiency(fast learning speed )
    Better generalization(random initialization)
  Multi-Layer
    Better accuracy
    Allows us to train Machine with more abstract & complicated information
Importance and Contribution of Preprocessing
  Feature extraction algorithm
  Well-refined dataset

## Slide 5: Experiments

## Slide 6: Training & Testing Algorithm
Input Vector
Target Vector
Training Algorithm
Input Vector
Training Algorithm
Predict Vector
a) Training
b) Testing
transplant trained
model
feature data
predicting
label data
feature data

## Slide 7: Raw vs. Preprocessed
Given data(Australia NEM data):
  Daily Max and Mean Temperature data ( 2 points/day)
  Daily power load data with 30 mins interval ( 48 points/day)
Raw data:
  ( 50 points/day)
Preprocessed data:
  (144 points/day)

## Slide 8: Results
RMSE & standard deviation score
  Better and stable RMSE score with Preprocessed data
  RLM, HELM, RNN show sufficient performance
 | Raw [RMSE / std] | Preprocessed [RMSE / std]
ELM | 0.41623872 / 0.221092336106 | 0.061202814 / 0.00329981860402
HELM | 0.22272991 / 0.0834939381997 | 0.061838965 / 0.00282407457971
Single Layer Perceptron Network | 6.30388 / 1.0803 | 1.86425 / 0.314612
Multiple Layer Perceptron Network | 27.0591 / 23.0247 | 2.2562 / 3.21933
Convolutional Neural Network | 4.61754 / 3.52584 | 2.63669 / 1.11987
Recurrent Neural Network | 0.0964969 / 0.00310329 | 0.0696449 / 0.00145637

## Slide 9: Results
ELM

## Slide 10: Results
HELM

## Slide 11: Results
Single Layer Perceptron Network

## Slide 12: Results
Multiple Layer Perceptron Network

## Slide 13: Results
CNN

## Slide 14: Results
RNN

## Slide 15: Think Backward
Why ELM and HELM are showing similar performance?
  Input data features are simple enough for ELM, and it does not need to take HELM approach.
Why RNN and HELM are showing similar performance?
  RNN is gradient based algorithm, which is slow and has a risk to stuck on local optima. But it use a technique called “weight sharing” through time and it shows excellent performance.

## Slide 16: Conclusions
All algorithms show better and stable RMSE score with preprocessed data.
ELM, HELM and RNN models show the best performance among six learning algorithms designed.
 We checked that it is able to get better performance from the same predictive model with only limited data if the data preprocessing process is used.
 The results show that the ELM, HELM and RNN models are most suitable for the power demand forecasting.

## Slide 20: Main

## Slide 21: Sub